## Slide 1: Student Competition: Code Generation Training
Exercises

## Slide 2: Exercise 1 - Introduction
Notes: Introduction – Speech Enhancement with Spectral Subtraction
Eliminating additive noise from an audio signal is a fundamental problem in audio signal processing. For example, the accuracy of a speech recognition system can drastically decrease in the presence of additive noise in the input speech signal. Therefore, it is highly desirable to provide some means of noise reduction in the front end of speech recognizers that operate under adverse conditions.
Speech signal with additive noise can be mathematically represented by
y(t) = x(t) + w(t)
where y(t) is the noisy speech, x(t) is the clean (i.e., desirable) speech, and w(t) is additive noise. Usually, the noise signal has characteristics that are better distinguishable from the clean speech signal in frequency domain. Since the Discrete Fourier Transform (DFT) is a linear transform,
Y(f) = X(f) + W(f)
Assuming that spectral properties of the noise signal are known, the problem of enhancing the speech signal becomes a simple subtraction in spectral domain,
X(f) = Y(f) - W(f)
The enhanced signal can now be constructed by taking the inverse Fourier Transform of X(f).
Navigate to the Exercises\Exercise1 folder.
Open noiseReduction.m and run it section by section. In this exercise the noise spectrum w is known and loaded from a MAT-file.
Try changing the overestimation gain factor (par.wOverEstGain) in line 7 of the init.m file. This controls the level of noise suppression. Use values in the range [1,4] and note how higher values cause more aggressive suppression, but at the same time distorts the speech signal. You can listen to the result by typing the following at the MATLAB® Command Window:
>> soundsc(xEnhanced)
Try
>> cd Exercise1
>> run noiseReduction.m

## Slide 3: Exercise 1
Notes: Code Generation with MATLAB – Speech Enhancement with Spectral Subtraction
Reference: Chapter 1
This exercise introduces a speech enhancement algorithm based on spectral subtraction. The speech is enhanced by subtracting the noise power spectrum W from the observed noisy speech signal Y.
X(f) = Y(f) - W(f)
Open speechEnhancement.m and use the %#codegen directive to check codegen compatibility. Notice the coder.cstructname function call in the MATLAB code. This function is used to name the C structure type generated from the MATLAB structure par.
Open the MATLAB Coder app. Select speechEnhancement.m as the entry-point function and click Next.
Choose noiseReduction.m as the script that calls the entry-point function to automatically define input types. Ensure the variable NFFT is defined as a constant equal to the value of NFFT in the MATLAB Workspace.
Follow the MATLAB Coder app workflow. Select Executable as the Build type to generate an executable that uses the following custom C source files included with the exercise:
  main.c
  speechEnhancement_Inputs.c
  Hint: You can do this in the Custom Code section of the code generation settings.
Run the generated executable in the MATLAB Command Window.
Bonus: Use the Convert to script option to generate a MATLAB script that replicates the steps taken above to generate code.
Try
>> edit speechEnhancement.m

## Slide 4: Exercise 1 - Solution
Notes: Solution – Code Generation with MATLAB – Speech Enhancement with Spectral Subtraction
Add the %#codegen directive to speechEnhancement.m
After MATLAB Coder automatically defines input types, click NFFT to define as a constant. Click to define  Define constant  NFFT.
Go to More Settings  Custom Code and add the custom C files under additional source files and save the settings. Choose Executable as the build type and click
To convert a MATLAB Coder project into a MATLAB script, click the Open action menu ( ) button in the top right corner and choose Convert to script…
Locate the generated file speechEnhancement_script.m in the Current Folder section of the MATLAB desktop.
Run the executable from MATLAB and view the output. >> !speechEnhancement.exe
Solution
>> cd solution
>> edit speechEnhancement.m

## Slide 5: Exercise 2
Notes: Customizing Generated Code for MATLAB – Speech Enhancement with Spectral Subtraction
Reference: Chapter 2
Navigate to the Exercises\Exercise2 folder
Open noiseReduction.m. Notice that the variable Tab has been declared as a global variable. There could be a chance in your workflow where you would like to use persistent variables instead of global variables. Delete this global declaration.
Declare Tab as persistent on line 4 in noiseEstimator.m and initialize it to the expression zeros(NFFT,par.D) if it is empty. Run noiseReduction.m again and make sure the speech enhancement algorithm still works as expected.
Add the %#codegen directive to all the relevant functions and check for code generation preparedness. Use the coder.inline command to ensure that spectralSubtraction.m and noiseEstimator.m are inlined in the generated code.
Open the MATLAB Coder app. Select speechEnhancement.m as the entry-point function and follow the MATLAB Coder App workflow to generate an executable that includes the following custom C source files:
  main.c
  speechEnhancement_Inputs.c
Click and set the code generation options to:
  Disable support for non-finite numbers
  Generate all functions into a single file
  Not generate an example main
Generate an executable. Run the generated executable in the MATLAB Command Window and view the output.
Try
>> cd Exercise2
>> run noiseReduction.m
>> edit noiseEstimator.m
>> edit spectralSubtraction.m

## Slide 6: Exercise 2 - Solution
Notes: Solution – Customizing Generated Code for MATLAB – Speech Enhancement with Spectral Subtraction
Declare Tab as persistent in noiseEstimator.m
Add the %#codegen directive and the line coder.inline('always') to both noiseEstimator.m and spectralSubtraction.m to inline both these functions in the generated code.
Click More Settings  Speed and disable the Support non-finite numbers option.
In Code Appearance, set Generated file partitioning method to Generate all functions into a single file.
In All Settings, set the Generate example main option to Do not generate an example main function.
Choose Executable as the Build type and click to build.
Solution
>> cd solution
>> edit noiseEstimator.m
>> edit spectralSubtraction.m
>> !speechEnhancement

## Slide 7: Exercise 3 – Introduction
Notes: Introduction – IIR Filter
This exercise introduces an infinite impulse response (IIR) filter that implements the following difference equation:
In the Z-domain, the filter is represented by the transfer function:
Parameters are typically determined by analyzing the application environment in which the filter will operate. To achieve a suitable parameter set, you should be aware of your input’s frequency range and aspired damping behavior of the filter.
In this example, we will assume that the system requires a low-pass filter that noticeably attenuates a frequency above roughly 0.1*Fs/2. With a sample time of 1 ms, which implies a sampling frequency of 1 kHz, this results in a frequency of roughly 50 Hz.
The simple IIR filter is a discrete filter with a single state. The model iir.slx is an implementation of this filter, which will be used throughout this course. Open the model and run the simulation to see the filter implementation in Simulink, and observe its performance.
Try
Open the iir.slx model.
>> iir
Simulate the model.

## Slide 8: Exercise 3
Notes: Code Generation with Simulink –
IIR Filter
Reference: Chapter 3
Generate code for the IIR filter model and call the generated code from a main function.
Open the IIR model iir.slx and change the solver to a fixed-step solver.
Select the ert.tlc (Embedded Coder) system target file.
Generate code for the model.
Examine the generated code with the model-to-code traceability. For example, find the implementation for the Unit Delay block in the IIR_filter subsystem, in the generated code.
Examine iir.c for implementation of model algorithm.
Identify the inputs, outputs, parameters, and intermediate signals in the model and generated code.
Run the generated iir.exe at the OS command prompt. Recall that, by default, the generated code does not call the entry point iir_step function and we need to modify the example main function or write our own main function to do that. (Terminate operation by pressing Ctrl+C in the MATLAB Command Window.)
Open the ert_main.c function inside the generated iir_ert_rtw folder.
Replace the ert_main.c function text from the examples shown in the example_main folder:
  ert_main1.c: This implements a counter, performs the IIR filter function on a constant input and displays the output.
  ert_main2.c: This calls data from an external source, performs the IIR filter function and displays the output. If trying this example, copy the input_data.h file also to the iir_ert_rtw folder.
Rebuild the model by running the iir.bat file in the iir_ert_rtw folder. This generates the new executable.
Run the newly generated executable iir.exe to see the results of the new main calling the generated code.
Try
>> iir
Generate code for the model using the steps in this page.

## Slide 9: Exercise 3 - Solution
Notes: Solution – Code Generation with Simulink – IIR Filter
Open iir.slx and select a fixed-step solver by going to the Model Configuration Parameters  Solver pane.
Select the ert.tlc system target file by going to the Model Configuration Parameters  Code Generation and then clicking the Browse button.
Generate code for the model by clicking the Build Model button.
Examine the generated code with model-to-code traceability. To do this right-click a block and select C/C++ code  Navigate to C/C++ code.
In the code generation report, navigate to iir_step function to see the implementation of model algorithm.
Identify the inputs, outputs, parameters, and intermediate signals in the model and generated code.
Run the generated iir.exe at the OS command prompt. >> !iir.exe
Rebuild the model with a new ert_main.c function:
  Replace ert_main.c in the iir_ert_rtw folder with contents in ert_main1.c or ert_main2.c file in the example main folder.
  Delete iir.exe in the exercise folder.
  Run the iir.bat from the iir_ert_rtw folder. >> !iir.bat
  Run the iir.exe file from the exercise folder. >> !iir.exe
Solution
Open the model in the Exercise3\solution folder.
>> iir
This model has all the properties saved to make it ready for generating code. Follow the steps in this page to generate code. Replace ert_main.c text to call it from a user main function.
Input
Output
Intermediate
Signal
Parameters

## Slide 10: Exercise 4
Notes: Customizing Generated Code with Simulink – IIR Filter
Reference: Chapter 4
Customize the generated code for the IIR filter model to meet specific requirements.
Open the IIR model iir_optCode.slx and generate code.
Inspect the interface for the iir_optCode_step function in iir_optCode.c and notice that it does not accept any inputs and return any outputs.
Change the prototype for this function to arg_y = iir_algo(inp) and generate code to verify.
Make the parameters b0 and a1 as tunable parameters. Use the provided script initTunableParams.m to create the necessary Simulink.Parameter variables. Generate code to verify.
Optimize the generated code by removing initialization and termination routines.
Optimize the generated code by removing support for complex data type.
Improve the readability of the generated code by turning off the Signal storage reuse option. Bonus: Create local temporary variables instead of storing them in a global structure.
Bonus: As a final step, try changing the code generation objectives shown in the image below and see the effect of setting different options.
Try
>> iir_optCode
Customize code for the model using the steps in this page.

## Slide 11: Exercise 4 - Solution
Notes: Solution – Customizing Generated Code with Simulink – IIR Filter
Open the IIR model iir_optCode.slx and generate code using the Build Model button.
In the code generation report notice the function signature for iir_OptCode_step function.
In R2018a* (in R2018b, this is done differently. Refer to next page), change the function signature by using the Configure Model Functions button in the Model Configuration Parameters  Code Generation  Interface pane as shown below.
Run the script initTunableParams.m to create the necessary Simulink.Parameter variables in the base workspace. Generate code to verify.
Optimize the generated code
  Remove initialization: Go to the Model Configuration Parameters  Code Generation  Optimization pane and enable the following 2 options:
  Remove termination: Go to the Model Configuration Parameters  Code Generation  Interface pane and disable Terminate function required option under Advanced parameters.
Remove support for complex data types by going to Model Configuration Parameters  Code Generation  Interface pane and disabling complex numbers option under Software environment  Support.
Turn off signal storage reuse option by going to the Model Configuration Parameters  Diagnostics  Simulation Target pane and disabling Signal Storage Reuse option under Advanced Parameters.
Solution
Open the iir_optCode.slx model in Exercise4\solution folder and generate code to see all the options discussed in this page.
>> iir_optCode

## Slide 12: Exercise 4 – Configuring Function Prototype in R2018b
Notes: Configuring Function Prototype in MATLAB R2018b and Later
In MATLAB R2018b the Configure Model Functions button is replaced with a different workflow as follows.
After generating code, click the Show Perspective views button on the bottom right of the model window.
Choose the Code Perspective View.
This view lets you perform code generation specific tasks from a single window. Look at the Embedded Coder Quick Help on the left to see what task you are interested in. In our case we will configure the prototype for the entry point functions. Click Go There and you will be taken to the Code – Mappings C pane at the bottom of the window. Click the Entry-Point Functions tab and click on the button. You will see the initialize, step and terminate functions. You will change the function prototype of iir_step next.
Click on function name iir_step and the 3 dots beside it. Then choose Configure Prototype. This opens the Configure C Step Function Interface window similar to R2018a in the previous page. After this, change the function signature as shown in the screenshots there (below step 3) to complete the task. Generate code to verify.

## Slide 13: Exercise 5
Notes: System Integration with Simulink – Range Sensor
Reference: Chapter 5
Exercise
The rangeSensorStart model implements a range measurement system. The two inputs are noisy data from a short-range and a long-range sensor. The model processes each sensor input individually and then uses information about the measured range to combine the two sensor readings into a more accurate estimate.
Open the rangeSensorStart model. Simulate it and explore the results.
Save the model with the name rangeSensor. This will ensure the provided C main file will call the code generated from your model.
Notice that the short and long range sensors are being processed by the same outlier removal algorithm and filter. Use model referencing to convert these blocks into a reusable component stored in a separate model file.
The sensor processing blocks have a sample time of 0.01 second while the Stateflow chart has a sample time of 0.05 second. Configure the top-level model to generate a separate function for each rate.
Replace the code in the automatically generated ert_main.c file with the code in the provided main_rangeSensor.c file. Rebuild the executable and run it.
Try
>> rangeSensorStart
>> edit main_rangeSensor.c

## Slide 14: Exercise 5 - Solution
Notes: Solution – System Integration with Simulink – Range Sensor
Convert the Sensor Processing subsystem into a separate model file as shown below.
Go to Simulation  Model Configuration Parameters. From the Solver pane, enable the Treat each discrete rate as a separate task option.
This will generate two entry point functions named rangeSensor_step0 and rangeSensor_step1, which are used by the code in main_rangeSensor.c.
Solution
>> rangeSensorSoln
>> edit main_rangeSensorSoln.c
rangeSensorProc.slx